## Slide 1
QNX RTOS POWERED CUSTOM FLIGHT CONTROLLER
K. Saathvik Vardhan
Nampally Rahul
Kukkadapu Sai Vinay
By Team Airborne

## Slide 2
2
PROBLEM STATEMENT
Current drone flight controllers are:
  Mostly closed hardware / proprietary firmware
  Limited real-time determinism in complex missions
  Hard to customize for research and experimentation
  Difficult to integrate advanced RTOS features
Our Goal
Design an open hardware flight controller using QNX RTOS that provides
  deterministic real-time control
  modular architecture
  high reliability
  flexible customization
Problem Statement no. 50 - Open Hardware Real-World System

## Slide 3
3
MOTIVATION
Drone control systems require:
  Hard real-time response
  Reliable sensor fusion
  Safe multi-threaded operation
  Predictable scheduling
QNX RTOS offers:
  Microkernel architecture
  Deterministic scheduling
  Reliable IPC
  Fault isolation
These features make QNX suitable for safety-critical systems like drones.
Why QNX RTOS for Drones?

## Slide 4
SYSTEM ARCHITECTURE
4
Sensors:
  BNO085 → Orientation & motion sensing
  MS5611 → Altitude estimation
  HMC5883L → Heading detection
  NEO-M8N → Global positioning
Actuators:
  BLDC Motors via ESC
Communication:
  SPI → IMU
  UART → GPS
  I2C → Barometer & Magnetometer
  iBUS → Receiver input
Controller:
Raspberry Pi 4
Hardware Architecture

## Slide 5
SYSTEM ARCHITECTURE
5
Software Architecture
Core components:
  Sensor Manager
  Sensor Fusion Module
  Flight Control Algorithm
  Motor Control Module
  Communication Manager
Each module runs as separate processes/threads.
Benefits:
  Fault isolation
  Easy debugging
  Real-time scheduling

## Slide 6
RTOS CONCEPTS USED
6
1. Processes & Threads
Separate processes for:
  sensor acquisition
  control algorithms
  communication
2. Scheduling
  Priority-based scheduling
  Control loop given highest priority
3. Inter-Process Communication (IPC)
Used for communication between modules:
  message passing
  shared memory
4. Resource Management
Safe access to:
  SPI bus
  UART
  I2C sensors

## Slide 7
THREAD ARCHITECTURE
7
High Priority Threads
  IMU Data Thread (400–1000 Hz)
  Control Loop Thread
Medium Priority Threads
  GPS Processing
  Sensor Fusion
Low Priority Threads
  Telemetry
  Logging
  Diagnostics
This ensures deterministic control timing.

## Slide 8
CONCLUSION
8
QNX RTOS based flight controller
Key contributions:
  modular architecture
  deterministic real-time performance
  scalable design
  improved reliability
This system demonstrates practical application of QNX RTOS concepts in real-world embedded systems.