## Slide 1
Fault Tolerance System for Aerial Vehicles
K. Saathvik Vardhan
Nampally Rahul
Kukkadapu Sai Vinay
By Team Airborne
MGIT

## Slide 2
2
PROBLEM STATEMENT
Modern aerial systems such as advanced drones and eVTOL platforms rely on traditional real-time operating systems like VxWorks, INTEGRITY RTOS, PikeOS, and Deos RTOS to achieve deterministic real-time performance.
However, these systems are built on static and tightly coupled architectural models, which impose significant limitations for next-generation, high-compute aerial platforms.
Problem Statement no. 50 - Open Hardware Real-World System
To address the limitations of traditional avionics RTOS architectures, this project implements a modular fault tolerance system in flight controllers on a Raspberry Pi 4 using QNX Neutrino RTOS, leveraging its microkernel architecture and synchronous message-passing IPC.

## Slide 3
Fault-Tolerant Real-Time Communication in QNX (RPi 4)
Platforms : Respberry Pi 4
RTOS : QNX Neutrino
Sensor : MPU9250 (I2C)
FOCUS :
  IPC(Message Passing)
  Fault Tolerance
  Latency & Jitter Analysis
  CPU Performance Monitoring
3

## Slide 4
SYSTEM ARCHITECTURE
4
Sensors:
    NEO-M8N → Global positioning
    MPU9250 → Client → Server
    MS5611 → Altitude estimation
    HMC5883L → Heading detection
Actuators:
    BLDC Motors via ESC
Communication:
    I2C → Barometer & Magnetometer
    iBUS → Receiver input
    SPI → IMU
    UART → GPS
Controller:
Raspberry Pi 4
Components
Process 2 (Client)
    Reads MPU9250 via I2C
Process 1 (Server)
  Receives data via message passing
Monitor Logic
    Detects failure & restarts client
Key Design
    Fully process-based (no shared memory for IPC)
    Modular & restartable

## Slide 5
5

## Slide 6
IPC – Message Passing
6
Mechanism
  MsgSend() → Client sends data
  MsgReceive() → Server receives
  MsgReply() → Acknowledgement
Advantages
  Synchronous → deterministic
  Built-in priority inheritance
  No race conditions
  Sensor data transferred reliably
  No shared memory dependency

## Slide 7
Fault Tolerance Mechanism
7
1. Problem
Client may stop sending data
2.Solution
  Server monitors message arrival time
  If timeout occurs:
    Restart client process
3.Implementation
  Timeout detection using timers
  Restart using process control
4.Result
  Self-healing system
  No full system restart needed

## Slide 8
Process Restart (Spawn & Slay)
8
Slay
  Terminates faulty client
Spawn
  Used to create client process
  Enables dynamic startup
Workflow
  Detect timeout
  slay client
  spawn client
Benefit
  Fault isolation
  Continuous operation

## Slide 9
Latency Measurement (Timers)
9
What is Latency?
Time from:
Client send → Server receive
Implementation
  Using Timers:
    ClockCycles
  Timestamp at:
    Send
    Receive
Output
  Latency in ms/µs
Importance
  Validates real-time performance

## Slide 10
Jitter Measurement
What is Jitter?
Variation in latency over time
Calculation
Jitter = variation between consecutive latencies
Implementation
  Store previous latency
  Compute difference
Optional Enhancement
  Use shared memory + mutex:
    For logging/analysis
Importance
  Stability of control systems
10

## Slide 11
CPU Usage Measurement in QNX
Methods
1. Using pidin
  Command:
  pidin -p <pid> times
  Shows CPU time per process
2. Using top
  Real-time CPU usage view
3. Programmatic Method
  Use:
    ClockCycles()
    clock_gettime()
Formula
CPU Usage = (Process Time / Total Time) × 100
11

## Slide 12
Results & Key Outcomes
  Reliable IPC using message passing
  Fault-tolerant restart mechanism
  Measured:
Latency
Jitter
  CPU usage
  Deterministic communication
  Modular design
  Real-time validation
12

## Slide 13
13

## Slide 14
14